## Slide 1: Welding Simulation with Kuka LBR iiwa 14 R820
-Varun Asthana
CNPM662: Project Presentation

## Slide 2: Robot Specifications
Maximum reach: 820mm
Maximum payload: 14kgs.
Kuka LBR iiwa 14 R820
Joint configuration of the arm-
RRRRRRR (7 revolute joints)
Constraints on angular positions

## Slide 3: Forward Kinematics

## Slide 4: Forward Kinematics
Why rotating x-axis again and again by 180 degrees?
Frame assignment and DH table formation
Due to the pre-defined local frames assigned to the joints in the vrep model
Correction of this by rotating the joints to simplify DH table was not feasible due to geometry deformation of the robot (because of pre-defined hierarchy tree of robot elements).
‘b’ represents the base frame, which is same as world frame
x2
x6
xb
zb
x0
z0
x1
z2
z1
x4a
z4a
x3
z3
x4
z4
x5
z6
zn
xn
z5

## Slide 5: Forward Kinematics
Frame assignment and DH table formation
Frame | Thetai-1 | di-1 | ai | Alphai
b-0 | 0 | db | 0 | 0
0-1 | 180 + t1 | 0 | 0 | 90
1-2 | 180 + t2 | 0 | 0 | 90
2-3 | 180 + t3 | d1 | 0 | -90
3-4a | 180 + t4 | 0 | 0 | -90
4a-4 | 0 | d2 | 0 | 0
4-5 | 180 + t5 | 0 | 0 | 90
5-6 | 180 + t6 | 0 | 0 | 90
6-n | t7 | dn | 0 | 0
DH Table
Let us denote the joint parameters by:
t1, t2, t3, t4, t5, t6 and t7 respectively for joints 1 to 7, starting from bottom to top.
(here ‘t’ stands for theta, measured in degree)
All A and T matrices are calculated using the above DH table.
‘b’ represents the base frame, which is same as world frame
xb
zb
x0
z0
x1
z2
z1
x4a
z4a
x3
z3
x4
z4
x5
z6
zn
xn
z5

## Slide 6: Inverse Kinematics

## Slide 7: Inverse Kinematics
Inverse Position and Inverse orientation decoupling
All the 3 highlighted axis coincide at a common point, called wrist center.
This allows the inverse kinematics problem to be decoupled into-
Inverse Position (bottom 4 joints), and
Inverse Orientation (top 3 joints)
Under constrained system
Inverse positions of wrist center Oc i.e. 3 variables (xc, yc. zc) are to be solved by using 4 joint parameters (t1 to t4). Hence infinite solutions exist.
Resolved with following assumption:
Locking joint 3, that is setting t3=0 degree

## Slide 8: Inverse Kinematics
Inverse Position
t1
t2
t2
-t4
d1
d2
db
xc
zc
yc
d2 sin(t2-t4)
d2 sin(t2-t4)
d1 sin(t2)
Oc
d1 cos(t2)
d2 cos(t2-t4)
xc = {d1*sin(t2) + d2*sin(t2-t4)}*cos(t1)
yc = {d1*sin(t2) + d2*sin(t2-t4)}*sin(t1)
zc = d0 + d1*cos(t2) + d2*cos(t2-t4)
Solving Inverse Position
t1 = atan2 (yc/xc)
t4 = acos {((xc^2) + (yc^2) + (zcc^2) - (d1^2) - (d2^2))/(2*d1*d2)}
t2 is obtained by solving a quadratic in cos(t2)
which is depends on cos(t4)
Unique Solution
2 Solutions
4 Solution
Note: These solutions occur in pairs

## Slide 9: Inverse Kinematics
t5 = atan2 (Rwrist(2,3)/Rwrist(1,3))
t6 = acos (Rwrist(3,3))
t7 = atan2 (Rwrist(3,2)/-Rwrist(3,1)) or
atan2 (-Rwrist(3,2)/Rwrist(3,1))
Inverse Orientation
Solving Inverse Orientation
2 Solutions
Rwist = [R74 ]T Rdb
RHS of above equation is known, and LHS is unknown. LHS is a function of t5, t6 and t7. Hence solved by comparing.
Unique Solution
2 Solutions
Note: These solutions occur in pairs
xb
zb
Defining Rdb It is assumed that-
Object is parallel to the ground
Welding will take place at 45o from the –xb axis and will be directed from top to bottom.
xn
zn
45o
Rdb = Rx(180) * Ry(45)

## Slide 10: Results
FK & IK solved in MATLAB
Simulation done in vrep
MATLAB Output

## Slide 11: Results
FK & IK solved in MATLAB
Simulation done in vrep
VREP Simulation- Multiple Position and Orientation

## Slide 12: Results
FK & IK solved in MATLAB
Simulation done in vrep
VREP Simulation- Path Planning

## Slide 13: Results
FK & IK solved in MATLAB
Simulation done in vrep
VREP Simulation
t1 = atan2 (yc/xc)
atan2 (-yc/-xc)
Unique Solution

## Slide 14: Thank You